## Slide 1: Computer Architecture Part 2
Jerry B. Backer
NYU Tandon School of Engineering

## Slide 2: Outline
Branch and Jump Instructions
Usages of Branch and Jump
Examples of Branch and Jump

## Slide 3: Instructions Covered So Far
Load Doubleword (LD)
Store Doubleword (SD)
Doubleword Add (DADD)
Doubleword OR (DOR)

## Slide 4: Other MIPS64 Instructions
Immediate ALU instructions: DADDI, DORI, DANDI
  Useful for operations using hardcoded values
    int x = 3; int y = x +17
    Immediate instruction hardcodes value of 17. No need for register

## Slide 5: Other MIPS64 Instructions
Immediate ALU instructions: DADDI, DORI, DANDI
  Useful for operations using hardcoded values
    int x = 3; int y = x +17
    Immediate instruction hardcodes value of 17. No need for register
  DADDI Rt, Rs, DoImm # Rt  Rs+ DoImm+
    Immediate is 16 bits
    It needs to be sign-extended before doing addition
    Use case: int x = 3; int y = x + 17
    Value 17 is hardcoded in instruction as: 00000000000010001

## Slide 6: Other MIPS64 Instructions
Immediate ALU instructions: DADDI, DORI, DANDI
  Useful for operations using hardcoded values
    int x = 3; int y = x +17
    Immediate instruction hardcodes value of 17. No need for register
  DADDI Rt, Rs, DoImm # Rt  Rs+ DoImm+
    Immediate is 16 bits
    It needs to be sign-extended before doing addition
    Use case: int x = 3; int y = x + 17
    Value 17 is hardcoded in instruction as: 00000000000010001
  DORI Rt, Rs, DoImm # Rt  Rs || DoImm
    Immediate is 16 bits
    For DORI, DANDI (and other boolean operations), immediate value is not sign-extended. It is padded with zeroes to make it 64 bits (zero-extension

## Slide 7: DADDI
DADDI Rt, Rs, DoImm # Rt  Rs+ DoImm+
  Immediate is 16 bits
  It needs to be sign-extended before doing addition

## Slide 8: Jump Instructions
Allow CPU to jump to specific locations in code
  Used for function calls, return from functions, if/else statements, case statements, interrupts, etc
Two types of JumpInstructions
  Unconditional: Always jump to location
  Conditional : Branch to location based on specific condition
Location to jump (target address) can be:
  Relative: Target is Func(PC, param1, param2)
  Indirect: Target is in register or memory.

## Slide 9: Jump Instructions
Allow CPU to jump to specific locations in code
  Used for function calls, return from functions, if/else statements, case statements, interrupts, etc
Two types of JumpInstructions
  Unconditional: Always jump to location
  Conditional : Branch to location based on specific condition
Location to jump (target address) can be:
  Relative: Target is Func(PC, param1, param2)
  Indirect: Target is in register or memory.

## Slide 10: MIPS64 Unconditional Jump Instructions
J Address: Jump at address based on address
  Semantics: PC Func1(PC, Address)
  Used for unconditional jump within a function (e.g. goto statements)
JAL Address: Jump and Link at address
  Semantics:
    R31  PC +4 ;
    PC  Func1(PC, Adress)
  Used to call functions
JR Rs: Jump at address in register
  Semantics: PC  Rs
  Used to return from function calls

## Slide 11: MIPS64 Unconditional Jump Target Address
JR Rs: Jump at address in register
  Semantics: PC  Rs
  Used to return from function calls
  Target is stored in register Indirect target

## Slide 12: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)

## Slide 13: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)
    Add PC +4
    Take most significant 4 bits from step 1 : PC+4[31:28]
    Do Address << 2  Address * 4 to make it 28 bits
    Concatenate results of steps 2 and 3

## Slide 14: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)
  Example: 4DC J 13B
    PC = 4DC 000004DC
    Address = 13B

## Slide 15: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)
  Example: 4DC J 13B
    PC = 4DC 000004DC
    Address = 13B
    Add PC +4 : 000004DC+ 4  000004E0
    Take most significant 4 bits from step 1 : 0x0

## Slide 16: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)
  Example: 4DC J 13B
    PC = 4DC 000004DC
    Address = 13B
    Add PC +4 : 000004DC+ 4  000004E0
    Take most significant 4 bits from step 1 : 0x0
    Do Address << 2 : 13B << 2
      13B*4  4EC
      Making it 28 bits : 00004EC

## Slide 17: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)
  Example: 4DC J 13B
    PC = 4DC 000004DC
    Address = 13B
    Add PC +4 : 000004DC+ 4  000004E0
    Take most significant 4 bits from step 1 : 0x0
    Do Address << 2 : 13B << 2
      13B*4  4EC
      Making it 28 bits : 00004EC
    Concatenate results of steps 2 and 3: 0x0000004EC

## Slide 18: MIPS64 Unconditional Jump Target Address
J and JAL Target Address
  PC Func1(PC, Address)
  Address parameter in Func1 is 26 bits
  Func1(PC, Address) = (PC+4)[31:28]||(Address << 2)
    Add PC +4
    Take most significant 4 bits from step 1 : PC+4[31:28]
    Do Address << 2  Address * 4 to make it 28 bits
    Concatenate results of steps 2 and 3

## Slide 19: MIPS64 Conditional Branch Instructions
BEQ Rs, Rt, DoImm:
  Semantics: If (Rs == Rt) PC  Func2(PC, DoImm)
  Used for if/else statements and loops
BNE Rs, Rt, DoImm:
  Semantics: If (Rs != Rt) PC  Func2(PC, DoImm)
  Used for if/else statements and loops
Many more: BEQZ, BNEQZ, BLTZ, BLETZ,…
We focus primarily on BEQ, BNEQ, BEQZ
Branch Taken
  Branch condition is true and CPU jumps to target
  i.e. BNE R8, R9, 3 # If R8 != R9, then branch is TAKEN

## Slide 20: MIPS64 Conditional Branch Instructions
BEQ Rs, Rt, DoImm:
  Semantics: If (Rs == Rt) PC  Func2(PC, DoImm)
  Used for if/else statements and loops
BNE Rs, Rt, DoImm:
  Semantics: If (Rs != Rt) PC  Func2(PC, DoImm)
  Used for if/else statements and loops
Many more: BEQZ, BNEQZ, BLTZ, BLETZ,…
We focus primarily on BEQ, BNEQ, BEQZ
Branch Taken
  Branch condition is true and CPU jumps to target
  i.e. BNE R8, R9, 3 # If R8 != R9, then branch is TAKEN

## Slide 21: MIPS64 Conditional Branch Target Address
BEQ Rs, Rt, DoImm
  PC Func2(PC, DoImm)
  DoImm parameter in Func2 is 16 bits
  Func2(PC, DoImm) = (PC+4)+ (DoImm+ << 2)

## Slide 22: MIPS64 Conditional Branch Target Address
BEQ Rs, Rt, DoImm
  PC Func2(PC, DoImm)
  DoImm parameter in Func2 is 16 bits
  Func2(PC, DoImm) = (PC+4)+ (DoImm+ << 2)
    Add PC +4
    Sign Extend DoImm to 32 bits : DoImm+
    Take result of step 2 and shift it left by 2 : DoImm+ << 2
    Add results of step 1 and 3

## Slide 23: MIPS64 Conditional Branch Target Address
BEQ Rs, Rt, DoImm
  PC Func2(PC, DoImm)
  DoImm parameter in Func2 is 16 bits
  Func2(PC, DoImm) = (PC+4)+ (DoImm+ << 2)
  Example: 400008 BEQ R8, R0, 1
    PC = 400008 00400008
    DoImm = 1 0x0001
    Add PC +4: 00400008 + 4 = 0040000C
    Sign-extend DoImm: 0x0001+ = 0x00000001

## Slide 24: MIPS64 Conditional Branch Target Address
BEQ Rs, Rt, DoImm
  PC Func2(PC, DoImm)
  DoImm parameter in Func2 is 16 bits
  Func2(PC, DoImm) = (PC+4)+ (DoImm+ << 2)
  Example: 400008 BEQ R8, R0, 1
    PC = 400008 00400008
    DoImm = 1 0x0001
    Add PC +4: 00400008 + 4 = 0040000C
    Sign-extend DoImm: 0x0001+ = 0x00000001
    Take result of step 2 and shift it left by 2
      Multiply 32-bit value by 4: 0x00000001*4 = 0x00000004
    Add results of steps 1 and 3: 0x004000010
      0040000C+0x00000004 = 0x400010

## Slide 25: MIPS64 Conditional Branch Target Address
BEQ Rs, Rt, DoImm
  PC Func2(PC, DoImm)
  DoImm parameter in Func2 is 16 bits
  Func2(PC, DoImm) = (PC+4)+ (DoImm+ << 2)
    Add PC +4
    Sign Extend DoImm to 32 bits : DoImm+
    Take result of step 2 and shift it left by 2 : DoImm+ << 2
    Add results of step 1 and 3

## Slide 26: MIPS64 SLT Instruction : Set Less Than
Syntax: SLT Rd, Rs, Rt
Semantics: if (Rs < Rt) Rd = 1; else Rd = 0

## Slide 27: MIPS64 SLT Instruction : Set Less Than
Syntax: SLT Rd, Rs, Rt
Semantics: if (Rs < Rt) Rd = 1; else Rd = 0
  BLTZ Rt, DoImm: Branch if less than equal to zero
    Combines SLT and BEQ to form itself
      SLT Rd, Rs, R0 # if (Rs < R0) Rd 1; else Rd 0
      BEQ Rd, R0, DoImm # If (Rd == 0) PC  Funct2(PC, DoImm)

## Slide 28: MIPS64 Branch/Jump Instruction Uses
int abs(int x) // return absolute value of x
{
if (x < 0) // x is negative
x = -x; // make it positive
return x; // done
}

## Slide 29: MIPS64 Branch/Jump Instruction Uses
int abs(int x) // return absolute value of x
{
if (x < 0) // x is negative  conditional branch needed
x = -x; // make it positive
return x; // done  jump JR needed
}

## Slide 30: MIPS64 Branch/Jump Instruction Uses
if (x < 0)
Assume that x is in R4.
We can do :
BLTZ R4, DoImm # If (R4<0), R4 is negative, go to part of code that does x = -x

## Slide 31: MIPS64 Branch/Jump Instruction Uses
if (x < 0)
Assume that x is in R4.
We can do :
BGEZ R4, R0, DoImm # If (R4>=0), R4 is positive, skip substraction and go to return x

## Slide 32: MIPS64 Branch/Jump Instruction Uses
if (x < 0)
Assume that x is in R4.
We can do :
SLT, R8, R4, R0 # if (R4 < 0 ) R8 =1, else R8 = 0
BEQ R8, R0, DoImm# If (R8 == R0), R4 is already positive, skip subtraction and jump to return x

## Slide 33: MIPS64 Branch/Jump Instruction Uses
400004 SLT R8, R4, R0 # If x < 0 , R8 =1 , else R8 = 0
400008 BEQ R8, R0, DoImm# If R4 is positive, go to return x
…….. # what do we do here?
…….. # or here?
….. # or there?

## Slide 34: MIPS64 Branch/Jump Instruction Uses
400004 SLT R8, R4, R0 # If x < 0 , R8 =1 , else R8 = 0
400008 BEQ R8, R0, DoImm# If R4 is positive, go to return x
…….. # what do we do here?
Handle case where BEQ condition is false
For the code above, that is the subtraction operation
If (x < 0) // x is negative
x = -x; // make it positive
return x; // done

## Slide 35: MIPS64 Branch/Jump Instruction Uses
400004 SLT R8, R4, R0 # If x < 0 , R8 =1 , else R8 = 0
400008 BEQ R8, R0, DoImm# If R4 is positive, go to return x
40000C DSUB DSUB R4, R0, R4 # x = 0 -x = x=-x
…….. # or here?
If (x < 0) // x is negative
x = -x; // make it positive
return x; // done

## Slide 36: MIPS64 Branch/Jump Instruction Uses
400004 SLT R8, R4, R0 # If x < 0 , R8 =1 , else R8 = 0
400008 BEQ R8, R0, DoImm# If R4 is positive, go to return x
40000C DSUB DSUB R4, R0, R4 # x = 0 -x = x=-x
…….. # or here?
Once subtraction is done, return from call
If x is positive, skip subtraction and return from call
This is thus where we return from call
If (x < 0) // x is negative
x = -x; // make it positive
return x; // done

## Slide 37: MIPS64 Branch/Jump Instruction Uses
400004 SLT R8, R4, R0 # If x < 0 , R8 =1 , else R8 = 0
400008 BEQ R8, R0, DoImm# If R4 is positive, go to return x
40000C DSUB DSUB R4, R0, R4 # x = 0 -x = x=-x
400010 JR Rs # return from abs() function call
If (x < 0) // x is negative
x = -x; // make it positive
return x; // done

## Slide 38: MIPS64 Branch/Jump Instruction Uses
400004 SLT R8, R4, R0 # If x < 0 , R8 =1 , else R8 = 0
400008 BEQ R8, R0, DoImm# If R4 is positive, go to return x
40000C DSUB DSUB R4, R0, R4 # x = 0 -x = x=-x
400010 JR Rs # return from abs() function call
Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+<<2)
Inverse of Func2: DoImm+ = [Target - (PC+4)] >> 2
DoImm+ = [400010 – (400008+4)] >> 2
DoImm+ = [400010 – 40000C] >> 2
DoImm+ = [4] >> 2  4/4
DoImm+ = 1
DoImm = 1

## Slide 39: MIPS64 Branch/Jump Instruction Uses
//lib.h
int abs(x);
//lib.c
int abs(x){ if (x < 0) x = -x; return -x;}
//main.c
include “lib.h” // include lib.h for abs(x)
int val, result; char buffer[50];
fgets(buffer, 50 stdin); //get input from user
val = atoi(buffer); //convert char array to int
result = abs(val); //JAL to call abs(x) in lib.c.
printf(“Absolute value: %d\n, result);
400004 SLT R8, R4, R0
400008 BEQ R8, R0, 1
40000C DSUB R4, R0, R4
400010 JR Rs # return x

## Slide 40: MIPS64 Branch/Jump Instruction Uses
//lib.h
int abs(x);
//lib.c
int abs(x){ if (x < 0) x = -x; return -x;}
//main.c
include “lib.h” // include lib.h for abs(x)
int val, result; char buffer[50];
fgets(buffer, 50 stdin); //get input from user
val = atoi(buffer); //convert char array to int
result = abs(val); //JAL to call abs(x) in lib.c.
printf(“Absolute value: %d\n, result);
400004 SLT R8, R4, R0
400008 BEQ R8, R0, 1
40000C DSUB R4, R0, R4
400010 JR 31 # return x
Recall: JAL Address:
R31  PC+4 # return address
PC = Func1(PC, Address)

## Slide 41: MIPS64 Branch/Jump Instruction Uses
Func2 calculates the target address of the branch instruction
Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+<<2)
Inverse of Func2: DoImm+ = [Target - (PC+4)] >> 2

## Slide 42: MIPS64 Branch/Jump Instruction Uses
val = atoi(buffer); //convert char array to int
result = abs(val); //JAL to call abs(x) in lib.c.
printf(“Absolute value: %d\n, result);
400004 SLT R8, R4, R0
400008 BEQ R8, R0, 1
40000C DSUB R4, R0, R4
400010 JR R31 # return x
Return value of abs(val) must be stored in result
Current MIPS code has value in R4
Recall: R4 is parameter register and does not hold value across function calls
Must use R2 or R3 to return value from abs(val) call

## Slide 43: MIPS64 Branch/Jump Instruction Uses
val = atoi(buffer); //convert char array to int
result = abs(val); //JAL to call abs(x) in lib.c.
printf(“Absolute value: %d\n, result);
400004 DADD R2, R4, R0 # R2 = x + 0
400008 SLT R8, R4, R0
40000C BEQ R8, R0, 1
400010 DSUB R2, R0, R4
400014 JR R31 # return x
Return value of abs(val) must be stored in result
Current MIPS code has value in R4
Recall: R4 is parameter register and does not hold value across function calls
Must use R2 or R3 to return value from abs(val) call

## Slide 44: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Do not use MIPS multiplication (MULT) instruction
  Goal is to learn how to use branch/jump instructions for loops

## Slide 45: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
int mult(int x, int y)
{ int res = 0, i=y;
while( i != 0)
{res+=x; i--; }
return res;
}

## Slide 46: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }while( i != 0);
return res;
}
int mult(int x, int y)
{ int res = 0, i=y;
while( i != 0)
{res+=x; i--; }
return res;
}

## Slide 47: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 48: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 49: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 50: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
4E0 BNE R9, R0, DoImm # if (i !=0), go to 4D8 for next addition
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 51: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
4E0 BNE R9, R0, DoImm # if (i !=0), go to 4D8 for next addition
4E4 … what to do here? # handle case where i = 0: loop done!
408 ... and here?
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 52: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
4E0 BNE R9, R0, DoImm # if (i !=0), go to 4D8 for next addition
4E4 ADD R2, R8, R0 # Use R2 to return value of res
408 ... and here?
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 53: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
4E0 BNE R9, R0, DoImm # if (i !=0), go to 4D8 for next addition
4E4 ADD R2, R8, R0 # Use R2 to return value of res
4E8 JR R31 #return from function call
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 54: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
4E0 BNE R9, R0, DoImm # if (i !=0), go to 4D8 for next addition
4E4 ADD R2, R8, R0 # Use R2 to return value of res
4E8 JR R31 #return from function call
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 55: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
4E0 BNE R9, R0, DoImm # if (i !=0), go to 4D8 for next addition
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}
Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+<<2)
Inverse of Func2: DoImm+ = [Target - (PC+4)] >> 2
DoImm+ = [4D8 – (4E0+4)] >> 2
DoImm+ = [4D8 – 4E4] >> 2
DoImm+ = [FFC] >> 2  -12/4
DoImm+ = -3
DoImm = -3

## Slide 56: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 DADD R8, R8, R4 # res+=x
4DC DADDI R9, R9, (-1)10 #i--;
4E0 BNE R9, R0, (-3)10 # if (i !=0), go to 4D8
4E4 ADD R2, R8, R0 # Use R2 to return value of res
4E8 JR R31 #return from function call
int mult(int x, int y)
{ int res = 0, i=y;
do {res+=x; i--; }
while( i != 0);
return res;
}

## Slide 57: MIPS64 Branch/Jump Instruction Uses
Consider two numbers x y, both > 0
Write the MIPS mnemonic code to perform x *y
Assume x is in R4, y is in R5
4D0 DADD R8, R0, R0 # res = 0
4D4 DADD R9, R5, R0 # i =y
4D8 BNE R9, R0, 1 # if i !=0, go to 4E0
4DC J 13B # i = 0, jump to 4EC
4E0 DADD R8, R8, R4 # res+=x
4E4 DADDI R9, R9, (-1)10 #i--;
4E8 J 136 # jump to beginning of loop at 4D8
4EC ADD R2, R8, R0 # R2 = res
4F0 JR R31 #return from function call
int mult(int x, int y)
{ int res = 0, i=y;
while( i != 0)
{res+=x; i--; }
return res;
}
loop instructions

## Slide 58: Topics Covered
Jump and Branch Instructions
  Fundamental in all architectures
  Indirect target and near/relative target addresses
  Allow for if/else statements, loops, function call, etc