## Slide 1
Computer Organization
CS-Bridge Program, Summer 2016
Introduction
Jerry Backer
jerry.backer@nyu.edu
Notes: Hi,
My name is Jerry and I will be your instructor for the Computer Architecture and Organization Section of the CS-Bridge Program.
So far, we have covered several paradigms and techniques of computer programming. And these techniques have enabled us
to write software code for different purposes. So what we will first cover in this section is how the CPU interprets this code and executes
it.
We will then discuss what is inside the CPU that allows it to execute such code.
1

## Slide 2
Topics Covered
  Assembly Language/Mnemonic
    Various assembly instructions
    Instruction Formats
  Processor (CPU) Organization
    CPU Execution Steps
    High-Level State Diagram
    CPU Pipelining
    Memory Hierarchy
Computer Organization
7/20/2016
2
Notes: More specifically, we will go over assembly language and mnemonic machine code, which are human-readable representations of machine-level instruction.
We will then go over the CPU execution steps and discuss the microarchitecture of the CPU
2

## Slide 3
A Little Bit of Background…
Computer Organization
7/20/2016
3
Functional Units
ALU
IMUL
FPU
FMUL
Notes: So.. let’s cover a little bit of background on computer architecture.
This is just for us to get a flavor of what’s inside of a CPU so we can get a better feel of assembly, its mnemonic notation and machine-level code.
So, at a high-level, there three main hardware components of a CPU: the functional units, the registers, and the memory hierarchy.
The functional units are hardware components that perform logic, arithmetic, and other operations
- Examples of functional units we may find are
* the Arithmetic Logic Unit , or ALU, which performs integer addition, subtraction and logic operations such as AND, OR, XOR, etc.
* the floating Point Unit, or FPU, which performs the same operations as the ALU, but for floating point data
* the integer multiplication unit, or IMUL, which performs integer multiplication and division
* then there is the floating multiplication unit, of FMUL, which performs floating point multiplications and divisions
3

## Slide 4
A Little Bit of Background…
Computer Organization
7/20/2016
4
Functional Units
GPRs
ALU
IMUL
FPU
FMUL
Notes: General purpose registers or GPRS, are components to store the data for the functional units
So every data that a functional unit operate on, must first be located in a general purpose register
Similarly, once a functional unit finishes an operation, it puts the result back in a general purpose register.
4

## Slide 5
A Little Bit of Background…
Computer Organization
7/20/2016
5
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
Notes: The other important component in the CPU is the memory hierarchy.
This hierarchy includes the hard disk, your main memory or RAM, and several other storage components known as caches.
The memory hierarchy stores both the software and the data of a given program and different levels of the hierarchy are used for different purposes.
For example, the hard disk is used for permanent storage and the RAM and caches are used for temporary storage.
We will cover specific aspects of the memory hierarchy towards the end of the computer architecture section
5

## Slide 6
A Little Bit of Background…
Computer Organization
7/20/2016
6
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
int b = 3;
int c = 4;
int a = b+c;
Notes: So, let us go through a simple example to illustrate how these three main components work in concert.
Let’s say we have a simple program, written in C or C++, such as the one we have next to the Memory block.
6

## Slide 7
A Little Bit of Background…
Computer Organization
7/20/2016
7
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
int b = 3;
int c = 4;
int a = b+c;
Notes: The crux of the code is to perform the addition b+c and to put the result back in memory location of a
7

## Slide 8
A Little Bit of Background…
Computer Organization
7/20/2016
8
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
int b = 3;
int c = 4;
int a = b+c;
Notes: Since b and c are integer values 3 and 4 respectively, the ALU functional unit will be used.
Remember that each data used by a functional unit must first be available in a general purpose register
So the first operations of the CPU are to move the data for b and c to general purpose registers
8

## Slide 9
A Little Bit of Background…
Computer Organization
7/20/2016
9
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
3
int b = 3;
int c = 4;
int a = b+c;
Notes: So, for the first operation to implement a = b+c is to copy the value of b into a general purpose register
9

## Slide 10
A Little Bit of Background…
Computer Organization
7/20/2016
10
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
3
4
int b = 3;
int c = 4;
int a = b+c;
Notes: The second operation copies the value of c into another general purpose register.
At this point, both values are in registers so the ALU can use them to do the addition
10

## Slide 11
A Little Bit of Background…
Computer Organization
7/20/2016
11
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
3
4
7
ADD
int b = 3;
int c = 4;
int a = b+c;
Notes: As we see here, in the operation, the ALU performs the addition of 3+4 and puts the result back into a general purpose register.
11

## Slide 12
A Little Bit of Background…
Computer Organization
7/20/2016
12
ALU
FPU
FMUL
GPRs
MEM
Memory
Hierarchy
IMUL
Functional Units
int b = 3;
int c = 4;
int a = b+c;
3
4
7
a=7
Notes: The last operation for this code is to copy the value of the result register back into the memory location for a
So in total, we have four operation to perform a = b+c
The first two operations copied the values of b and c into the registers, because the functional units only operate on data that are in general purpose registers
The next operation performs the addition and puts the result into a general purpose register,
and the last operation copies the value of the result from its register to memory
12

## Slide 13
A Little Bit of Background…
Computer Organization
7/20/2016
13
CPU Design Strategy:
  Reduced Instruction Set Computing (RISC)
  Complex Instruction Set Computing (CISC)
Notes: So, let us quickly go over the most two types of CPU architectures in the market.
One is called Reduced Instruction Set Computing or RISC
and the other is called Complex Instruction Set Computing, or CISC.
The decision of which of those architecture to use impacts how the machine-level instructions of the CPU work, how the hardware and data path of the CPU is implemented, and how the compiler for that CPU works
13

## Slide 14
A Little Bit of Background…
Computer Organization
7/20/2016
14
RISC: Reduced Instruction Set Computing
  Recall 4 operations for a = c +c
  Reduced: single operation per instruction
  Benefits:
      Simple hardware (for simpler instructions)
      One cycle per instruction (pipelined)
  Issues:
      More complicated compilers
      Larger binary
Notes: Let us first discuss the RISC architecture.
the basic idea of RISC is to have simple instructions that perform simple operations.
Let us recall the a = b+c function from before.
In a RISC processor, each of the four operations needed to implement this function can be considered as an instruction.
So there would be an instruction to load b to register, and instruction load c to register, and instruction to add data b and c and put the result back in a register, and an instruction to store the result back to a
The benefit of having instructions that perform simple operations is that they make it easy to implement the CPU at the hardware level
So the CPU hardware is less complex and incurs less power and space in you computer
The main downside is that it is more difficult to translate the high-level code into machine-level instructions/ This makes the work of compilers more difficult.
The most ppopular RISC architecture is ARM, which is commonly found in smartphones, tablets, and other low-power or battery-powered platforms
14

## Slide 15
A Little Bit of Background…
Computer Organization
7/20/2016
15
CISC: Complex Instruction Set Computing
  Recall 4 operations for a = b +c
  Complex: multiple operations per instruction
    i.e. One instruction can do both memory access and addition of b and c
  Benefits:
      Easy translation from software to machine code
      Smaller binary (because less instructions do more operations)
  Issues:
      More complicated hardware
      Many-cycle instructions
Notes: CISC architecture does the reverse of RISC
That is, it has very complex machine level instructions, where an instruction can perform multiple operations.
For example, an instruction can do both a memory access operation and an addition operation.
The main benefit of this is that it makes it easier to translate high-level code, such as c into machine instructions, simplifying the compiler.
The downside is that the hardware of the CPU is more complex because of the multiple operations that an instruction can perform.
The most popular CISC architecture is x86 from Intel.
15

## Slide 16
What We Have Covered:
    Main components of CPU Hardware
    Role of General Purpose Registers
    RISC vs. CISC
Computer Organization
7/20/2016
16
Notes: So we have gone over a high-level view of the most important components of a generic CPU,
discussed general purpose registers and the functionality and we have
differentiate RISC and CISC computer architecture.
In this class, we will use a RISC architecture known as MIPS to cover the different topics.
Thanks
16

## Slide 17
Computer Organization
CS-Bridge Program, Summer 2016
Assembly Language – Part 1
Jerry Backer
jerry.backer@nyu.edu
Notes: Hi everyone,
In this module, we will introduce some basic concepts of assembly programming and then correlate to machine-level programming using a mnemonic format
17

## Slide 18
What We’ll Learn
  Introduction to MIPS Assembly Language
  MIPS Mnemonic Machine Code
  Fundamental MIPS Machine Instructions
  MIPS Registers and their Roles
Computer Organization
7/20/2016
18
Notes: More specifically,
We will introduce some basic assembly instructions in the MIPS architecture,
We will then go in detail on how to map MIPS assembly into MIPS mnemonic format, which is the format we will be focusing on throughout the class.
18

## Slide 19
Computer Organization
7/20/2016
19
MIPS Instruction Set Architecture
Microprocessor Without Interlocked Pipeline Stages
  RISC Processor Architecture Developed by MIPS Technologies
  32-bit and 64-bit versions
  Used in gaming systems (NS64, PS1, PS2, etc), set-top boxes, and other embedded systems
  MIPS64 architecture used in this class
Notes: So, MIPS stands for Microprocessor Without Interlocked Pipeline Stages.
Later on in this computer architecture section, we will discuss the concept of pipelining in CPUs.
MIPS has both 32-bit and 64-bit versions. This means that some version of MIPS can do operations only on data that are at most 32 bits, whereas other MIPS versions can perform operations on data as bit as 64 bits.
MIPS is very popular in gaming systems such as play station, 1, 2, and portable, some gaming system from Nintendo, and various arcade games.
19

## Slide 20
MIPS Assembly: introductory example
Computer Organization
7/20/2016
20
int a, b, c;
b = 0x65E;
c = 0x2C;
a = 0x0;
a = b+c ;
High-level code
Notes: So, let’s go through a detailed example of converting a high-level code to MIPS assembly and ultimately to MIPS mnemonic format.
Consider the high-level code above. Note that the values for a, b, and c, are initialized in hexadecimal format
20

## Slide 21
MIPS Assembly: introductory example
Computer Organization
7/20/2016
21
int a, b, c;
b = 0x65E;
c = 0x2C;
a = 0x0;
a = b+c ;
High-level code
Compilation Process
Software Binary
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
11011101000010010000000000000000 11011101000010100000000000000100
00000001001010100101100000101100
11111100101100000000000000001000
Notes: So when we compile this high-level C/C++ code, we get the software binary
And if we try to open this binary, what we see is a bunch of ones and zeros representing the bits for the machine code that implements this high-level code
21

## Slide 22
MIPS Assembly: introductory example
Computer Organization
7/20/2016
22
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
Code Segment
Data Segment
b= 0x65E
c= 0x2C
a= 0x0
0xF00
0xA000
11011101000010010000000000000000 11011101000010100000000000000100
00000001001010100101100000101100
11111100101100000000000000001000
Notes: This binary itself is broken down into two segments:
a code segments that contains the machine level instructions that implement the functionality of the high-level code
and a data segment that contains the declared static variables in the high-level code.
As the figure indicates, each segments has a start or base address. In our example, the code segment base address is F00 and the base address of the data segment is A000.
22

## Slide 23
MIPS Assembly: introductory example
Computer Organization
7/20/2016
23
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
Code Segment
Data Segment
b= 0x65E
c= 0x2C
a= 0x0
??? a= b+c ????
0xF00
0xA000
11011101000010010000000000000000 11011101000010100000000000000100
00000001001010100101100000101100
11111100101100000000000000001000
Notes: So ideally, what we would like to do is to be able to understand the high-level code a =b+c in its machine code format
23

## Slide 24
MIPS Assembly: introductory example
Computer Organization
7/20/2016
24
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
Code Segment
Data Segment
b= 0x65E
c= 0x2C
a= 0x0
0xF00
0xA000
11011101000010010000000000000000 11011101000010100000000000000100
00000001001010100101100000101100
11111100101100000000000000001000
??? a= b+c ????
Notes: However, this is too complicated because working with bits over time is tedious and error prone
24

## Slide 25
MIPS Assembly: introductory example
Computer Organization
7/20/2016
25
Assembly Language
  Symbolic Machine Code
  Low-level programming language
  One-to-one correlation with machine-level code
  Mnemonics used to represent machine code
Notes: So for this class, we will use MIPS64 assembly.
Each MIPS64 instruction is 32-bits long, but the data can be as much as 64 bits
25

## Slide 26
MIPS Assembly: introductory example
Computer Organization
7/20/2016
26
Recall that MIPS is RISC Architecture
a = b+c:
  Copy b from data segment to register $t1
  Copy c from data segment to register $t2
  Add $t1 and $t2 and put result in $t3
  Copy $t3 to data segment address for a
Notes: So let use the a = b+c example to illustrate MIPS64 assembly.
Recall that MIPS is a RISC architecture, so there must be four operations to perform a =b+c : 2 to load b and c to registers, one to add the registers, and one to store the result back to memory location of a
So there are four MIPS instructions needed to implement this high-level c code.
The first instruction copies the value of b from the data segment to a register; let us assume it uses register t1.
The second instruction copies the value of c from the data segment to another register, say register t2
At this point, the value of b and c are in t1 and t2 respectively
The third instruction adds the the registers t1 and t2 and puts the result into register t3
The last instruction copies the value of t3 into the data location that is allocated for a
26

## Slide 27
MIPS Assembly: introductory example
Computer Organization
7/20/2016
27
Recall that MIPS is RISC Architecture
a = b+c:
  Copy b from data segment to register $t1 LD $t1, b
  Copy c from data segment to register $t2 LD $t2, c
  Add $t1 and $t2 and put result in $t3 DADD $t3, $t2, $t1
  Copy $t3 to data segment address for a SD $t3, a
Notes: SO given that there is a one-to-one correlation between the machine instruction and the assembly language,
we see an assembly instruction for each operation needed to perform the high-level code.
The first assembly instruction is Load doubleword, or LD $t1, b. In this instance, double indicates that the value in b is a double word, or is 64 bits long.
The second instruction Load doubleword $t2, a.
The third instruction is doubleword add or DADD t2 and t1 and put the answer in t3.
And the last instruction is store doubleword or SD the content of t3 into memory address of a.
Note the syntax of the instructions.
For load doubleword, we see the destination register is put first, followed by the label of the memory address
For the doubleword add, the destination register is put first, followed by the the source register operands,
For the Store Doubleword, the source register is put first, followed by the label of the destination memory location
27

## Slide 28
MIPS Assembly: introductory example
Computer Organization
7/20/2016
28
Recall that MIPS is RISC Architecture
a = b+c:
  LD $t1, b
  LD $t2, c
  DADD $t3, $t2, $t1
  SD $t3, a
11011101000010010000000000000000 11011101000010100000000000000100
00000001001010100101100000101100
11111100101100000000000000001000
Notes: So, since assembly language has a one to one correlation to machine code, we can map each assembly instruction of the a =b+c function to a machine-level instruction
28

## Slide 29
MIPS Assembly: introductory example
Computer Organization
7/20/2016
29
  LD $t1, b
MIPS Machine code
MIPS Assembly
11011101000010010000000000000000
Notes: However, assembly code doesn’t fully represent machine-level instruction.
Let us consider for example one of the Load doubleword instructions we had earlier and let’s compare it to the real machine instruction.
Using this example, we will see that the assembly instruction doesn’t have some of the fields of the machine-level instruction.
29

## Slide 30
MIPS Assembly: introductory example
Computer Organization
7/20/2016
30
  LD $t1, b
  Opcode
MIPS Machine code
MIPS Assembly
11011101000010010000000000000000
110111
opcode
✓
LD
Notes: The most significant six bits of the machine-level instruction represent the its opcode . The opcode is a simple mnemonic label to encode the operation of the of the instruction. In this case,
the opcode 110111 is associated for load double word instruction. The assembly instruction also has the load doubleword opcode.
30

## Slide 31
MIPS Assembly: introductory example
Computer Organization
7/20/2016
31
  LD $t1, b
  Opcode
  Base Register
MIPS Machine code
MIPS Assembly
11011101000010010000000000000000
110111
opcode
01000
base
✓
✗
LD
R8
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
0xA000
Base address
Data Segment
Notes: The next 5 bits of the assembly-level instruction represent the base field. This is the register number that stores the base address of the data segment.
In the machine-level instruction, this base register is register number 8, or R8. Note that there is no such field in the assembly instruction. Instead, it simply uses the label name of the
data as it was declared in the high-level code. The CPU cannot understand such high-level label.
31

## Slide 32
MIPS Assembly: introductory example
Computer Organization
7/20/2016
32
  LD $t1, b
  Opcode
  Base Register
  Rt register
MIPS Machine code
MIPS Assembly
11011101000010010000000000000000
110111
opcode
01000
base
01001
Rt
✓
✗
LD
R8
R9
✓
Notes: The next 5 bits of the machine-level instruction represent the Rt register field. This field indicates the destination register where the double word will loaded.
In the machine-level instruction, this Rt register is register number 9 or R9 and it is labeled as t1 in the assembly code. This is still quite similar to the machine code
32

## Slide 33
MIPS Assembly: introductory example
Computer Organization
7/20/2016
33
  LD $t1, b
  Opcode
  Base Register
  Rt register
  Offset
MIPS Machine code
MIPS Assembly
11011101000010010000000000000000
110111
opcode
01000
base
01001
Rt
0000000000000000
offset
✓
✗
✗
LD
R8
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
0xA000
Data Segment
R9
offset
0x0
✓
Notes: The last 16 bits of the machine code is the offset field. It indicates where within the data segment the requested value is located.
In our example, the offset is 0 because b is the first value in the data segment.
Note that the assembly-level instruction does not have such field.
33

## Slide 34
MIPS Assembly: introductory example
Computer Organization
7/20/2016
34
From Assembly to Mnemonic Format
    Maps assembly code to Machine Code
    Better represents CPU innerworkings
    Uses Hexadecimal notation
      except for register numbers
      except if explicitly stated otherwise
        i.e. FFFF in hex = (-1)10
Notes: So, although assembly-language provides a one-to-one correlation with machine code, it still has some limitations with fully illustrating how the CPU interprets the instructions.
And since this is a computer architecture and organization course, we want to have as good of a feel as possible of the CPU innerworkings.
With that in mind, we use MIPS mnemonic format to represent software code.
We can think of MIPS mnemonic as a readable version of machine-level code.
It interprets all of the fields of machine-level code to better illustrate the innerworkings of the CPU.
When writing in MIPS mnemonic notation, we generally use hexadecimal format, except for register names.
For some cases, the hexadecimal notation of number may take some space. In such cases, we use the decimal notation of that number and explicitly say it is the decimal notation.
For example FFF in hexadecimal is -1 in decimal, so we put -1 in parentheses and add the 10 subscript to indicate this a decimal number. This is just to make it easier
to write in MIPS mnemonic format
34

## Slide 35
MIPS Assembly: introductory example
Computer Organization
7/20/2016
35
MIPS Mnemonic
  LD $t1, b
  LD $t2, c
  DADD $t3, $t2, $t1
  SD $t3,a
MIPS Assembly
  F00 LD R9, 0(R8)
  F004 LD R10, 8(R8)
  F008 DADD R11, R9, R10
  F00C SD R11, (16)10 (R8)
a = b+c;
High-level C/C++
Notes: Let us now go over an example of MIPS mnemonic in detail.
The figure on the right is the MIPS mnemonic version of our assembly working example.
We notice some clear differences from the offset.
35

## Slide 36
MIPS Assembly: introductory example
Computer Organization
7/20/2016
36
MIPS Mnemonic
  LD $t1, b
  LD $t2, c
  DADD $t3, $t2, $t1
  SD $t3,a
MIPS Assembly
  F00 LD R9, 0(R8)
  F004 LD R10, 8(R8)
  F008 DADD R11, R9, R10
  F00C SD R11, (16)10 (R8)
a = b+c;
High-level C/C++
instruction addresses
Notes: The first thing we notice is that each instruction has an associated address. This is the address of the instruction in the code segment.
Note that these addresses are in byte and they are represented in hexadecimal.
36

## Slide 37
MIPS Assembly: introductory example
Computer Organization
7/20/2016
37
10001101000010010000000000000000 10001101000010100000000000000100
00000001001010100101100000100000
10100000101100000000000000001000
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
Code Segment
Data Segment
b= 0x65E
c= 0x2C
a= 0x0
a= b+c;
F00
F00+4
F00+4+4
F00+4+4+4
A000
Notes: Remember that since each instruction is 32 bits, or four bytes, it is easy to calculate the address of each instruction once we know the base address of the code segment. The base address itself is the address of the first instruction of the segment
37

## Slide 38
MIPS Assembly: introductory example
Computer Organization
7/20/2016
38
MIPS Mnemonic
  LD $t1, b
  LD $t2, c
  DADD $t3, $t2, $t1
  SD $t3,a
MIPS Assembly
  F00 LD R9, 0(R8)
  F004 LD R10, 8(R8)
  F008 DADD R11, R9, R10
  F00C SD R11, (16)10 (R8)
a = b+c;
High-level C/C++
Notes: We also notice that the registers are given using their numbers, as is done in machine code.
There are 32 general purpose registers in MIPS64, so they are numbered R0 to R31
38

## Slide 39
MIPS Assembly: introductory example
Computer Organization
7/20/2016
39
MIPS Mnemonic
  LD $t1, b
  LD $t2, c
  DADD $t3, $t2, $t1
  SD $t3,a
MIPS Assembly
  F00 LD R9, 0(R8)
  F004 LD R10, 8(R8)
  F008 DADD R11, R9, R10
  F00C SD R11, (16)10 (R8)
a = b+c;
High-level C/C++
offset
base
Notes: The last thing we notice is that the mnemonic notation has the same fields as the machine code.
Using the first Load doubleword example, we see that the mnemonic notation has the base and offset fields, just like the machine code discussed earlier
39

## Slide 40
MIPS Assembly: introductory example
Computer Organization
7/20/2016
40
Code Segment
F00
F04
F08
F0C
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
Data Segment
b= 0x65E
c= 0x2C
a= 0x0
A000
Notes: Here we put the full version of the code segment in MIPS mnemonic notation. The semicolon indicates the beginning of a comment.
So anything following the semicolon is a comment. This is similar to the forward slash in C or C++ We will go over the meaning of the instructions and the comments soon.
40

## Slide 41
MIPS Assembly: introductory example
Computer Organization
7/20/2016
41
Code Segment
F00
F04
F08
F0C
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
0000000000000000000000000000000000000000000000000000011001011110
0000000000000000000000000000000000000000000000000000000000101100
0000000000000000000000000000000000000000000000000000000000000000
Data Segment
b= 0x65E
c= 0x2C
a= 0x0
A000
A000+8
A000+8+8
Notes: Regarding the data segment, we know that each data is 64 bits, or 8 bytes, because we are using MIPS64. So once we know the base address of the data segment, we can find the addresses of all data in the segment. Note that this is the same approach that the CPU uses to determine the address of data, by using the base address of the data segment and the offset of the target data within that segment.
41

## Slide 42
MIPS Assembly: introductory example
Computer Organization
7/20/2016
42
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Notes: So putting it all together, we get the following notation for the code and data segments in MIPS mnemonic.
Note that all addresses are in hexadecimal.
42

## Slide 43
What We Have Covered:
    Introduction to MIPS Assembly Language
    Basic MIPS instructions: LD, DADD, SD
    Introduction to MIPS Mnemonic
Computer Organization
7/20/2016
43
Notes: we have introduced mips assembly language and covered some fundamental instructions.
We have also seen that, although assembly has a one-to-one correlation to machine level code, it
doesn’t fully illustrate how the CPU executes the code.
We have then covered MIPS mnemonic notation, which gives a good middle ground between assembly and machine-level code.
Next, we will use a tabular approach to illustrate how the CPU updates registers and memory when it executes instructions
43

## Slide 44
Computer Organization
CS-Bridge Program, Summer 2016
Assembly Language – Part 2
Jerry Backer
jerry.backer@nyu.edu
Notes: Hi everyone,
We will now pick up from the MIPS mnemonic notation and start discussing some aspects of CPU execution.
44

## Slide 45
What We’ll Learn
  MIPS Mnemonic Execution Structure
  Syntax and Semantics of LD, DADD, and SD
  MIPS General Purpose Registers R0-R31
Computer Organization
7/20/2016
45
Notes: We will use a table to show how the CPU updates registers and memory when executing instruction.
We will then discuss the three instructions we have covered so far and detail their fields and how they work
Finally, we will review the 32 MIPS general purpose registers and what their roles are
45

## Slide 46
MIPS Assembly: introductory example
Computer Organization
7/20/2016
46
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Notes: So last time we were here and we showed how MIPS mnemonic notation
46

## Slide 47
MIPS Assembly: introductory example
Computer Organization
7/20/2016
47
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
All contents of table are in Hexadecimal
  except for register numbers
  except if used explicit subscript notation (e.g. 1610 for decimal notation)
Notes: We will now show how to execute this MIPS code in table representative of the components of the CPU.
So the table has the following columns:
- an instruction column that lists the instructions of the MIPS
a PC column, where PC stands for program counter. the Program Counter is a special register in the CPU that contains the address of the next instruction to execute.
Then, there is a column for each register used in the MIPS mnemonic code. Since our example uses registers R8, R9, and R10, there is a column for each.
There is also a column for each data in the data segment. Since there are 3 pieces of data in the data segment, there are three columns and we use their addresses to label each
The last column is a memory access column to indicate what kind of memory access the associated instruction makes.
Since we are using the MIPS mnemonic format for the table, the content of the table will be in hexadecimal, unless stated otherwise using the subscript notation.
47

## Slide 48
MIPS Assembly: introductory example
Computer Organization
7/20/2016
48
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial |  |  |  |  |  |  |  |  | 
Notes: The first column of the table is ALWAYS the Initial column. This column illustrates the state of the CPU before execution.
48

## Slide 49
MIPS Assembly: introductory example
Computer Organization
7/20/2016
49
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial |  |  |  |  |  | 65E | 2C | 0 | 
Notes: The first column of the table is ALWAYS the Initial column. This column illustrates the state of the CPU before execution.
At that state, the data segment has the original data of the variables in the code. So we write those values in their respective columns in the table.
49

## Slide 50
MIPS Assembly: introductory example
Computer Organization
7/20/2016
50
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
Memory is passive: It does no computation; it only stores data
At initialization, CPU writes address of first to PC register
At initialization, CPU writes base address of data segment to R8
Notes: In addition, the CPU writes the first instruction of the code in the PC register and writes the base address of the data segment in the R8 register.
Remember that the PC stores the address of the next instruction to execute. So since the next instruction to execute is the first one, it make since that PC has that address
before any instruction is executed.
Regarding the value of R8, we see that the MIPS mnemonic code uses R8 as the base register for load doubleword , as well as store double instruction. So we write the base address of the data segment in R8
Since we don’t initialize the values of theother registers, we set them as question marks. This is because we don’t know what they are and some other program may have written values in them.
50

## Slide 51
MIPS Assembly: introductory example
Computer Organization
7/20/2016
51
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) |  |  |  |  |  |  |  |  | Ins read
For each instruction, CPU reads memory to get the instruction (Ins read)
Notes: For each instruction, the first the CPU does is it reads the instruction from the code segment; that is known as an instruction fetch or instruction read, concatenated as Ins read in the memory access column.
The CPU uses PC to get the address of the instruction to read
51

## Slide 52
MIPS Assembly: introductory example
Computer Organization
7/20/2016
52
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 |  |  |  |  |  |  |  | Ins read
For each instruction, CPU reads memory to get instruction (Ins read)
For most instructions, CPU increments PC (by 4) to point to next instruction
Notes: Since the PC register points to the address of the next instruction, once an instruction is fetched, the PC has to be updated to point to the next instruction. Generally, this update is done by simply incrementing the PC by 4, because instructions are 4 bytes long. Later in this course, we will when PC is not always incremented by 4 due to branch and jump instructions.
52

## Slide 53
MIPS Assembly: introductory example
Computer Organization
7/20/2016
53
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 |  |  |  |  |  |  | NS | Ins read/Data read
LD R9, 0(R8)
  Calculate address of data : R8+0 => A000 + 0 = A000
  Read data from memory address calculate: M[A000]
Notes: We then observe the instruction to see what it does.
It’s a load double instruction, where the offset is 0, the base is R8, and the destination register is R9.
So, the CPU first calculates the address of the data in memory. This is done by adding the content of the base register to the offset.
Once the address is obtained, the CPU reads the memory at that address to get the data. Since this is a memory access, we update the memory access column to indicate a data read.
53

## Slide 54
MIPS Assembly: introductory example
Computer Organization
7/20/2016
54
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 |  | 65E |  |  |  |  |  | Ins read/Data read
LD R9, 0(R8)
  Calculate address of data : A000 + 0 = A000
  Read data from memory address calculate: M[A000]
  Copy data to destination register: R9 = M[A000] = 65E
Notes: Once the data is obtained from memory, the CPU is written into its destination register.
54

## Slide 55
MIPS Assembly: introductory example
Computer Organization
7/20/2016
55
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 | NS | 65E | NS | NS | NS | NS | NS | Ins read
Registers and memory segments not modified are labeled NS: Not Stored
Notes: For all registers and memory locations that are not modified by this instruction, we put an NS to indicate Not Stored. In other words, this instruction does not store anything in those registers and data locations and their values are the same as before
55

## Slide 56
MIPS Assembly: introductory example
Computer Organization
7/20/2016
56
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 | NS | 65E | NS | NS | NS | NS | NS | Ins read
Notes: So at the end of this instruction, we see the value of R9 has been updated as desired by the Load doubleword and the program counter points to the next instruction. The program counter is very important because it is what the CPU uses to fetch the instructions.
56

## Slide 57
MIPS Assembly: introductory example
Computer Organization
7/20/2016
57
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 | NS | 65E | NS | NS | NS | NS | NS | Ins read/Data read
LD R10, 8(R8) | F08 | NS | NS | 2C | NS | NS | NS | NS | Ins read/Data read
Notes: The next instruction is also a load double word and we see that the memory access column indicates an instruction read to fetch the instruction from the code segment, and a data read, to read the double word data from the data segment
In addition, we see that the PC is incremented by four to point to the next instruction to execute and we see that the destination register R10 of the load doubleword is updated with the appropriate value. Everything else remains unchanged.
57

## Slide 58
MIPS Assembly: introductory example
Computer Organization
7/20/2016
58
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 | NS | 65E | NS | NS | NS | NS | NS | Ins read/Data read
LD R10, 8(R8) | F08 | NS | NS | 2C | NS | NS | NS | NS | Ins read/Data read
DADD R11, R9,R10 | F0C | NS | NS | NS | 68A | NS | NS | NS | Ins read
DADD R11, R9, R10
  Add content of source registers: R9+R10
  Store content of addition to destination Registers R11 = R9+R10
Notes: The next instruction is a Doubleword add.
This instruction takes R9 and R10, send them to the ALU for addition, takes the result and puts it back into the R11 destination register.
Note the syntax of the instruction: the destination register R11 is put first, followed by the two sources. We will discuss this syntax later.
The instruction only does an instruction read because it doesn’t access the data segment. Its operands are only registers. Generally, only load and store instructions perform data reads and writes.
We see the PC is incremented to point to the next instruction and R11 has the result of the addition in hexadecimal.
58

## Slide 59
MIPS Assembly: introductory example
Computer Organization
7/20/2016
59
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 | NS | 65E | NS | NS | NS | NS | NS | Ins read/Data read
LD R10, 8(R8) | F08 | NS | NS | 2C | NS | NS | NS | NS | Ins read/Data read
DADD R11, R9,R10 | F0C | NS | NS | NS | 68A | NS | NS | NS | Ins read
SW R11, (16)10 (R8) | F10 | NS | NS | NS | NS | NS | NS | 68A | Ins read/ Data Write
Notes: The last instruction is a store doubleword.
It works in a similar fashion to load doubleword, except that instead of loading from memory to register, it stores from register to memory.
Store doubleword uses its base register and offset to calculate the target address of the memory, then writes the content of the store register to the memory location indicated by the calculated address.
As a Store doubleword, the CPU does an instruction read and data write for this instruction.
We also see that the PC is incremented by 4, even if there is no such instruction at address F10 in our code segment. This is because this increment is done automatically by the CPU.
59

## Slide 60
MIPS Assembly: introductory example
Computer Organization
7/20/2016
60
Code Segment
Data Segment
65E
2C
0
F00
F04
F08
F0C
A000
A008
A010
  LD R9, 0(R8) ; R9 = M[R8+0]
  LD R10, 8(R8) ; R10 = M[R8+8]
  DADD R11, R9, R10 ; R11 = R9+ R10
  SD R11, (16)10 (R8) ; M[R8+1610] = R11
Instruction | PC | R8 | R9 | R10 | R11 | M[A000] | M[A008] | M[A010] | Memory Access
Initial | F00 | A00 | ? | ? | ? | 65E | 2C | 0 | --
LD R9, 0(R8) | F04 | NS | 65E | NS | NS | NS | NS | NS | Ins read/Data read
LD R10, 8(R8) | F08 | NS | NS | 2C | NS | NS | NS | NS | Ins read/Data read
DADD R11, R9,R10 | F0C | NS | NS | NS | 68A | NS | NS | NS | Ins read
SW R11, (16)10 (R8) | F10 | NS | NS | NS | NS | NS | NS | 68A | Ins read/ Data Write
Notes: At the end, this is content of the table.
It illustrates the different registers and memory locations that are relevant to the code and how they are impacted by each instruction in said code.
Later, we will do more table examples with different MIPS instructions.
60

## Slide 61
MIPS Assembly: introductory example
Computer Organization
7/20/2016
61
LD: Load Double Word
  Double Word = 64 bits
  Syntax: LD, Rt, Offset(Rs) i.e.: LD R9, 0(R8)
  Semantics: GPR[Rt] = M [Rs+SignExtended(Offset)]
    Offset is at most 16 bits
    Content of Rs is 64 bits
    Addition requires both data to be same size: 64bits
    Sign Extension: extend sign of 16-bit data to 64 bits while keeping sign (+/-)
        Example 1: 16-bit data: 0x8. SignEtxtended(0x0008) = 0x0000000000000008
        Example 2: 16-bit data: 0xAF00. SignEtxtended(0xAF00) = 0xFFFFFFFFFFFFAF00
        Example 3: 16-bit data 0xF00. SignEtxtended(0x0F00) = 0x0000000000000F00
Notes: Let us now discuss the syntax and semantics of the Load doubleword, doubleword add, and store doubleword instruction in MIPS
So we see the syntax and semantics of the the Load doubleword. Rs contains the base address of the data segment and the offset is position of the date relative to that base address. The offset is always at most 16 bits.
To calculate the address of the target data, the CPU adds the value of the base address in Rs to the offset. But Rs is a 64-bit register, and the offset is 16 bits. The addition requires both values to the same size. To change the size of the 16-bit offset to 64 bits, we perform a sign extension.
The basic idea of a sign extension is to increase the number of bits used to represent a value, while keeping the sign. Naively, the approach would to simply add enough zero bits to the left of the value until the number of bits desired is reached. However, this doesn’t work for negative numbers. This is because if we extend a negative number with zero bits, then it becomes positive because the most significant bit is now 0 instead of 1. So sign extension works by first looking at the most significant bit of a binary, and use the value of that bit to extend it to the desired bitsize.
The three examples here show how to sign extend different 16-bit values to 64 bits
61

## Slide 62
MIPS Assembly: introductory example
Computer Organization
7/20/2016
62
DADD: Double Word Add
  Syntax: DADD, Rd, Rs, Rt i.e.: DADD R11, R9, R10
  Semantics: GPR[Rd] = Rs + Rt
    Addition requires both data to be same size: 64bits
    GPR[Rd] = Rs + Rt
Notes: The double word add instruction adds two registers Rs and Rt and puts their result into Rd register.
62

## Slide 63
MIPS Assembly: introductory example
Computer Organization
7/20/2016
63
SD: Store Double Word
  Syntax: SD, Rt, Rs(Offset) i.e.: SD R11, 1610(R8)
  Semantics: M[Rs+SignExtended(Offset)] = Rt
    Addition requires both data to be same size: 64bits
    Use of sign extension to update 16-bit offset to 64 bits
Notes: The store doubleword instruction has the same syntax as load double word but the semantics are obviously different. Store doubleword copies the content of register Rt to the memory location indicated by the address calculated.
Similar to Rd, the calculation of the address requires the offset to be sign extended to 64 bits.
63

## Slide 64
MIPS Assembly: introductory example
Computer Organization
7/20/2016
64
MIPS General Purpose Registers: R0-R31
  R0: Always contains value 0; read-only
  R1: Reserved (used for pseudo instructions of assembler)
  R2-R3: Return results of function calls
  R4-R7: Pass parameters of function calls
  R8-R15: Store temporary values, not saved when function ends
  R16-R23: Store saved values across functions
  R24-R25: Store temporary values, not saved when functions
  R26-R27: Reserved (used by O.S.)
  R28: Global pointer
  R29: Stack pointer
  R30: Frame pointer
  R31: Return address
Notes: Let us know go over the list of general purpose registers in the MIPS CPU.
Remember there are 32 of them R0-R31.
R0 always contain the value 0 and it is read-only. That is, no code can write to it. It is only used whenever we want to use the value 0.
R1 is reserved for the assembler
R2 and R3 are used to return results of function calls. If you have a function that returns a an integer, then it will be stored in either R2 or R3 after the function completes.
One interesting question is how to have a function that returns a larger entity, like a struct of say 10 integers. I will leave it to you guys to find out how MIPS does it
R4-R7 are used to pass parameters of a function call. Similarly, I will let you guys find out how to call a function that passes more than four parameters.
R8 to R15 and R24 to R25 are used to store temporary values that are declared in a function. SO when then function completes, the values of these registers are not saved. We will primarily use these registers in our MIPS mnemonic codes.
R16 to R23 are used to store values in functions as well, but they are saved when the function completes.
R26 and R27 are reserved for the O.S
R28 is the global pointer and it points to the static data segment
R29 and R30 point to the stack and frame pointers respectively. The stack and frames are structures in the CPU that store local variables of a given function.
R31 stores the address to return from a function call.
For our course, we will primarily use R0, R8 to R15, R24, R25, and R31
Note that we do not include PC int this list because it is not a general purpose register. It is a special register and cannot be accessed by any user-level or O.S. level code
64

## Slide 65
MIPS Assembly: another example
Computer Organization
7/20/2016
65
Write MIPS mnemonic machine program for the operation above
  Code segment starts at address 0xC0
  Data segment starts at address 800
  Data stored in following order in memory: a, b, c
  Assume 64-bit data
  Data initial values: a = 4F0D, b= 14A0, c = 0
  Show table that details CPU work for each instruction (including initial state)
  Show final value in table
  Show comments of each mnemonic instruction as done in initial example
  Pay attention which registers not to use (eg. R0, R1, or R31)
a = b | c;
Notes: As an exercise,
I am encouraging you guys to try the following exercise.
First, write the MIPS Mnemonic code that performs the high-level code above. This code does a = b or c.
Note that this is logic or operation.
Once you have written the mnemonic code, show its execution in the table as we did before for a = b+c
The code and data segment addresses are specified, as well as the original values of a, b, and c
65

## Slide 66
What We Have Covered:
    CPU Execution Using Table
    LD, SD, and DADD Semantics
    PC Register and MIPS GPRs
Additional Documentation
  MIPS registers, assembly names and purposes
  MIPS64 instruction set
Computer Organization
7/20/2016
66
Notes: There is a document on the course site that summarize the 32 MIPS general purpose register and I also added the official documentation of the MIPS64 instruction set architecture
If you guys have any questions regarding anything we discuss, don’t hesitate to send me an e-mail.
Thanks,
66