## Slide 1: Computer Organization Part 1
Jerry B. Backer
NYU Tandon School of Engineering

## Slide 2: Outline
Instruction Types/Formats
Instruction Execution Steps
Processor State Diagram
Processor Clock Rate

## Slide 3: MIPS64 Instructions
All instructions are 32 bits
Instruction components
  Opcode: 6 leftmost bits
  2nd opcode/function (optional)
  Operands
    Immediate values
    register numbers
3 types of MIPS64 instructions
  R-format (register format)
  I-format (immediate format)
  J-format (jump format)

## Slide 4: MIPS64 Instruction Type: R-format
Uses ONLY register operands
  can be source, destination, or both
Fixed opcode: 000000
  For all R-format instructions
  2nd opcode (function) needed

## Slide 5: MIPS64 Instruction Type: R-format
Function: 2nd opcode
  Unique to each R-format instruction
  Indicates operation of instruction
Registers: Rs, Rt, and Rd
Shamt: shift amount
  Used only for SLL and SRL
  Otherwise, it is set to zero (0)
000000
Rs
Rt
Rd
shamt
6
5
5
5
5
6
opcode
Func

## Slide 6: MIPS64 Instruction Type: R-format
Opcode: 000000  R-format
000000
01000
01001
01011
00000
6
5
5
5
5
6
opcode
101100

## Slide 7: MIPS64 Instruction Type: R-format
Opcode: 000000  R-format
Func: 10110022  DADD
  DADD Rd, Rs, Rt # Rd  Rs + Rt
  No need for Shamt
000000
01000
01001
01011
00000
6
5
5
5
5
6
opcode
101100

## Slide 8: MIPS64 Instruction Type: R-format
Opcode: 000000  R-format
Func: 10110022  DADD
  DADD Rd, Rs, Rt # Rd  Rs + Rt
  No need for Shamt
Rs: 0100  R8
Rt: 0100  R9
Rd: 01011  R11
000000
01000
01001
01011
00000
6
5
5
5
5
6
opcode
101100
DADD R11, R8, R9

## Slide 9: MIPS64 Instruction Type: R-format
Function: 2nd opcode
  Unique to each R-format instruction
  Indicates operation of instruction
Registers: Rs, Rt, and Rd
Shamt: shift amount
  Used only for SLL and SRL
  Otherwise, it is set to zero (0)
000000
Rs
Rt
Rd
shamt
6
5
5
5
5
6
opcode
Func

## Slide 10: MIPS64 Instruction Type: I-format
Opcode
  Unique to each I-format instruction
  Indicates operation of instruction
Registers: Rs and/or Rt
DoImm: Immediate
  Always 16 bits
  ADDI, BEQ, and others
opcode
Rs
Rt
DoImm
6
5
5
16

## Slide 11: MIPS64 Instruction Type: I-format
Opcode: 011000  DADDI
011000
01000
10000
1111111111111100
6
5
5
16

## Slide 12: MIPS64 Instruction Type: I-format
Opcode: 011000  DADDI
  DADDI Rt, Rs, Imm # Rt
  Rt Rs + Imm+
Rs: 01000 R8
Rt: 10000 R16
011000
01000
10000
1111111111111100
6
5
5
16

## Slide 13: MIPS64 Instruction Type: I-format
011000
01000
10000
1111111111111100
6
5
5
16
DADDI, R16, R8, (-3)10
Opcode: 011000  DADDI
  DADDI Rt, Rs, Imm # Rt
  Rt Rs + Rt + Imm+
Rs: 01000 R8
Rt: 10000 R16
DoImm:11111111111111100
  FFFC
  (-3)10

## Slide 14: MIPS64 Instruction Type: J-format
Opcode
  Unique to each J-format instruction
  Indicates operation of instruction
No registers
Address
  Always 26 bits
  Used for target address of jump
opcode
Address
6
26

## Slide 15: MIPS64 Instruction Type: J-format
000010
00000100000000000000000000
6
26
Opcode: 000010 J
  J Address
Address: 0x10000
J 10000

## Slide 16: MIPS64 Instruction Type: J-format
Opcode
  Unique to each J-format instruction
  Indicates operation of instruction
No registers
Address
  Always 26 bits
  Used for target address of jump
opcode
Address
6
26

## Slide 17: Let’s Build a Processor
Based on MIPS64
Instructions Used
  DADD, DSUB, DOR, DAND
  LD, SD
  BEQZ

## Slide 18: Let’s Build a Processor: Instruction Execution Steps
Instruction Fetch (IF)
  Get Instruction From memory
  Increment Program counter
Instruction Decode (ID)
  Determine operation
  Get operands
Instruction Execute (EX)
  Perform operation
Memory (MEM)
  Do Data memory access
  For Load and Store instructions
WriteBack (WB)
  Write result to register

## Slide 19: Let’s Build a Processor: Instruction Execution Steps
Instruction Fetch (IF)
  Get Instruction From memory
  Increment Program counter
Instruction Decode (ID)
  Determine operation
  Get operands
Instruction Execute (EX)
  Perform operation
Memory (MEM)
  Do Data memory access
  For Load and Store instructions
WriteBack (WB)
  Write result to register

## Slide 20: Let’s Build a Processor: Instruction Fetch
Get instruction from memory
  M[PC]

## Slide 21: Let’s Build a Processor: Instruction Fetch
Get instruction from memory
  IR M[PC]
    IR: Instruction Register
    Special purpose register
    Holds 32-bit value of instruction

## Slide 22: Let’s Build a Processor: Instruction Fetch
Get instruction from memory
  IR M[PC]
Increment Program Counter
  PC  PC + 4

## Slide 23: Let’s Build a Processor: Instruction Decode
Determine operation
  Get opcode/2nd function
  Get values of operands
  Allocate functional units needed
  For our CPU, only one unit: ALU
    For arithmetic and logic operations
    Calculate address of BEQ, LD, SD
    2 outputs : ALUOut1, ALUOut2

## Slide 24: Let’s Build a Processor: Instruction Decode
Determine operation
Get operands
  A  GPR[Rs]
  B  GPR[Rt]
  Imm  DoImm+

## Slide 25: Let’s Build a Processor: Instruction Execution Steps
Instruction Fetch (IF)
  Get Instruction From memory
  Increment Program counter
Instruction Decode (ID)
  Determine operation
  Get operands
Instruction Execute (EX)
  Perform operation
Memory (MEM)
  Do Data memory access
  For Load and Store instructions
WriteBack (WB)
  Write result to register

## Slide 26: Let’s Build a Processor: Instruction Execute
Different for each instruction
Perform computation
  Arithmetic operation
  Logic operation
  2 outputs: ALUOut1, ALUOut2

## Slide 27: Let’s Build a Processor: Instruction Execute
EX: LD and SD
  Calculate address for load/store
    LD Rt, DoImm(Rs)
    SD Rt, DoImm(Rs)
  Address: Rs + DoImm+

## Slide 28: Let’s Build a Processor: Instruction Execute
EX: LD and SD
  Calculate address for load/store
    LD Rt, DoImm(Rs)
    SD Rt, DoImm(Rs)
  Address: Rs + DoImm+
    Recall: A  GPR[Rs] from ID
    Recall: Imm DoImm+ from ID
  ALUout1  A + Imm

## Slide 29: Let’s Build a Processor: Instruction Execute
EX: DADD, DSUB, DOR, DAND
  R-format logic/arithmetic op.
    DADD Rd, Rs, Rt # Rd  Rs+ Rt
    DSUB Rd, Rs Rt # Rd  Rs – Rt
    DOR Rd, Rs, Rt # Rd  Rs OR Rt
    DAND Rd, Rs, Rt # Rd  Rs AND Rt
  Recall: A GPR[Rs] from ID
  Recall: B  GPR[Rt] from ID

## Slide 30: Let’s Build a Processor: Instruction Execute
EX: DADD, DSUB, DOR, DAND
  R-format logic/arithmetic op.
    DADD Rd, Rs, Rt # Rd  Rs+ Rt
    DSUB Rd, Rs Rt # Rd  Rs – Rt
    DOR Rd, Rs, Rt # Rd  Rs OR Rt
    DAND Rd, Rs, Rt # Rd  Rs AND Rt
  Recall: A GPR[Rs] from ID
  Recall: B  GPR[Rt] from ID
000000
Rs
Rt
Rd
shamt
Func

## Slide 31: Let’s Build a Processor: Instruction Execute
EX: DADD, DSUB, DOR, DAND
  R-format logic/arithmetic op.
    DADD Rd, Rs, Rt # Rd  Rs+ Rt
    DSUB Rd, Rs Rt # Rd  Rs – Rt
    DOR Rd, Rs, Rt # Rd  Rs OR Rt
    DAND Rd, Rs, Rt # Rd  Rs AND Rt
  Recall: A GPR[Rs] from ID
  Recall: B  GPR[Rt] from ID
  ALUOut2  A Func B
000000
Rs
Rt
Rd
shamt
Func

## Slide 32: Let’s Build a Processor: Instruction Execute
EX: BEQZ Rs , DoImm
  Calculate target address
  Check branch condition
  Update program counter

## Slide 33: Let’s Build a Processor: Instruction Execute
EX: BEQZ Rs , DoImm
  Calculate target address
  Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+ << 2)
  Recall: PC  PC +4 in IF
  Recall: Imm  DoImm+ in ID
  ALUOut1 PC + (Imm << 2)

## Slide 34: Let’s Build a Processor: Instruction Execute
EX: BEQZ Rs , DoImm
  Calculate target address
  Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+ << 2)
  Recall: PC  PC +4 in IF
  Recall: Imm  DoImm+ in ID
  ALUOut1 PC + (Imm << 2)
  Check branch condition
    Zero flag in ALU
    Raised when ALU result is zero

## Slide 35: Let’s Build a Processor: Instruction Execute
EX: BEQZ Rs , DoImm
  Calculate target address
  Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+ << 2)
  Recall: PC  PC +4 in IF
  Recall: Imm  DoImm+ in ID
  ALUOut1 PC + (Imm << 2)
  Check branch condition
    Zero flag in ALU
    Raised when ALU result is zero
  Zero  A BranchOp R0

## Slide 36: Let’s Build a Processor: Instruction Execute
EX: BEQZ Rs , DoImm
  Calculate target address
  Recall: Func2(PC, DoImm) = (PC+4) + (DoImm+ << 2)
  Recall: PC  PC +4 in IF
  Recall: Imm  DoImm+ in ID
  ALUOut1 PC + (Imm << 2)
  Check branch condition
    Zero flag in ALU
    Raised when ALU result is zero
  Zero  A BranchOp R0
  Update program counter
  If Zero PC ALUOut1

## Slide 37: Let’s Build a Processor: Instruction Execute
EX: BEQZ Rs , DoImm
  Calculate target address
  ALUOut1 PC + (Imm << 2)
  Check branch condition
    Zero flag in ALU. 1-bit flag
    Raised to 1 when ALU result is zero. Else, it is set to 0
  Zero  A BranchOp R0 # A – R0
  Update program counter
  If Zero PC ALUOut1

## Slide 38: Let’s Build a Processor: Instruction Memory
MEM: LD
  LD Rt, Rs, DoImm
    GPR[Rt] M[Rs + DoImm+]
  Recall: ALUOut1A +Imm in EX
  LMD  M[ALUOut1]
    LMD: Load Memory Double
    Hold data obtained from memory

## Slide 39: Let’s Build a Processor: Instruction Memory
MEM: SD
  SD Rt, Rs, DoImm
    M[Rs + DoImm+] Rt
  Recall: ALUOut1A +Imm in EX
  Recall: B  GPR[Rt] in ID
  M[Aluout1] B

## Slide 40: Let’s Build a Processor: Instruction WriteBack
WB: LD
  LD Rt, Rs, DoImm
    GPR[Rt] M[Rs + DoImm+]
  Recall: LMDM[ALUOut1] in MEM
  GPR[Rt] LMD

## Slide 41: Let’s Build a Processor: Instruction WriteBack
WB: DADD, DOR, DAND, DSUB
  DADD Rd, Rs, Rt # Rd  Rs + Rt
  Data in in ALUOut2 after EX
  GPR[Rd]  ALUOut2

## Slide 42: Let’s Build a Processor: High-Level Diagram
Break execution steps into states
Label each state (numerically)
Transition between states according to instruction

## Slide 43: Let’s Build a Processor: High-Level Diagram
IR ← M[PC]
PC ← PC+4
0
IF
A← GPR[Rs]
B ← GPR[Rt]
Imm ← DoImm+
ID
1
LD,SD
ALUOut1 ← A+Imm
EX
2
LMD ←M[ALUOut1]
MEM
LD
GPR[Rt]← LMD
WB
4
0
3
M[ALUOut1]←B
5
0
SD
A/L
R-format
6
ALUOut2 ← A func B
GPR[Rd]← ALUOut2
0
ALUOut1 ← PC+Imm << 2
Zero ← A BranchOp 0
If Zero, PC ← ALUOut1
Zero ← 0
BEQZ
8
0
7

## Slide 44: Processor Clock Rate
Operating frequency of CPU
Speed for each operation
  1 GHz
  1/ 1*109 = 1 ns
  1 clock cycle = 1 ns
  1 cycle: time for each state in high-level state diagram

## Slide 45: Processor Clock Rate
IR ← M[PC]
PC ← PC+4
0
IF
A← GPR[Rs]
B ← GPR[Rt]
Imm ← DoImm+
ID
1
LD,SD
ALUOut1 ← A+Imm
EX
2
LMD ←M[ALUOut1]
MEM
LD
GPR[Rt]← LMD
WB
4
0
3
M[ALUOut1]←B
5
0
SD
A/L
R-format
6
ALUOut2 ← A func B
GPR[Rd]← ALUOut2
0
ALUOut1 ← PC+Imm << 2
Zero ← A BranchOp 0
If Zero, PC ← ALUOut1
Zero ← 0
BEQZ
8
0
7
LD, R9, 0(R8)

## Slide 46: Processor Clock Rate
IR ← M[PC]
PC ← PC+4
0
IF
A← GPR[Rs]
B ← GPR[Rt]
Imm ← DoImm+
ID
1
LD,SD
ALUOut1 ← A+Imm
EX
2
LMD ←M[ALUOut1]
MEM
LD
GPR[Rt]← LMD
WB
4
0
3
M[ALUOut1]←B
5
0
SD
A/L
R-format
6
ALUOut2 ← A func B
GPR[Rd]← ALUOut2
0
ALUOut1 ← PC+Imm << 2
Zero ← A BranchOp 0
If Zero, PC ← ALUOut1
Zero ← 0
BEQZ
8
0
7
LD, R9, 0(R8)
States: 0  1  2 3  4
5 clock cycles

## Slide 47: Processor Clock Rate
Code Segment: a = b|c
C0 LD R9, 8(R8)  5 cycles
C4 LD R10, (16)10(R8)  5 cycles
C8 DOR R11, R9, R10  4 cycles
CC SD R11, 0(R8)  4 cycles
Total  18 cycles

## Slide 48: Processor Performance
Code Segment: a = b|c
C0 LD R9, 8(R8)  5 cycles
C4 LD R10, (16)10(R8)  5 cycles
C8 DOR R11, R9, R10  4 cycles
CC SD R11, 0(R8)  4 cycles
Total  18 cycles
Is this fast?
The processor of a typical smartphone
can execute 4 instructions/cycle
THIS IS NOT FAST!!!!

## Slide 49: Processor Performance
IR ← M[PC]
PC ← PC+4
0
IF
A← GPR[Rs]
B ← GPR[Rt]
Imm ← DoImm+
ID
1
LD,SD
ALUOut1 ← A+Imm
EX
2
LMD ←M[ALUOut1]
MEM
LD
GPR[Rt]← LMD
WB
4
0
3
M[ALUOut1]←B
5
0
SD
A/L
R-format
6
ALUOut2 ← A func B
GPR[Rd]← ALUOut2
0
ALUOut1 ← PC+Imm << 2
Zero ← A BranchOp 0
If Zero, PC ← ALUOut1
Zero ← 0
BEQZ
8
0
7
LD, R9, 0(R8)
DADD R9, R9 R0

## Slide 50: Processor Performance
Methods to Improve Performance
  Pipelining
  Superscalar
  Speculative Execution
  Out-of-Order Execution
  Multithreading
  Multicore

## Slide 51: Processor Pipelining
Pipelined Execution
Instruction-level parallelism (ILP)
Execution steps broken down into stages
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) |  |  |  |  | 
C4 LD R10, (16)10(R8) |  |  |  |  | 
C8 DOR R11, R9, R10 |  |  |  |  | 
CC SD R11, O(R8) |  |  |  |  | 

## Slide 52: Processor Pipelining
Pipelined Execution
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 |  |  |  | 
C4 LD R10, (16)10(R8) |  |  |  |  | 
C8 DOR R11, R9, R10 |  |  |  |  | 
CC SD R11, O(R8) |  |  |  |  | 

## Slide 53: Processor Pipelining
Pipelined Execution
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 |  |  | 
C4 LD R10, (16)10(R8) |  |  |  |  | 
C8 DOR R11, R9, R10 |  |  |  |  | 
CC SD R11, O(R8) |  |  |  |  | 

## Slide 54: Processor Pipelining
Pipelined Execution
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 |  |  | 
C4 LD R10, (16)10(R8) | 2 |  |  |  | 
C8 DOR R11, R9, R10 |  |  |  |  | 
CC SD R11, O(R8) |  |  |  |  | 

## Slide 55: Processor Pipelining
Pipelined Execution
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 |  | 
C4 LD R10, (16)10(R8) | 2 | 3 |  |  | 
C8 DOR R11, R9, R10 | 3 |  |  |  | 
CC SD R11, O(R8) |  |  |  |  | 

## Slide 56: Processor Pipelining
Pipelined Execution
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 | 4 | 5
C4 LD R10, (16)10(R8) | 2 | 3 | 4 | 5 | 6
C8 DOR R11, R9, R10 | 3 | 4 | 5 | 6 | 7
CC SD R11, O(R8) | 4 | 5 | 6 | 7 | 

## Slide 57: Processor Pipelining
Pipelined Execution
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 | 4 | 5
C4 LD R10, (16)10(R8) | 2 | 3 | 4 | 5 | 6
C8 DOR R11, R9, R10 | 3 | 4 | 5 | 6 | 7
CC SD R11, O(R8) | 4 | 5 | 6 | 7 | 

## Slide 58: Processor Pipelining - Hazards
Conflicts of execution in pipeline
  Structural hazards
  Data hazards
  Branch hazards

## Slide 59: Processor Pipelining - Hazards
Conflicts of execution in pipeline
  Structural hazards
  Data hazards
  Branch hazards

## Slide 60: Processor Pipelining – Structural Hazards
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 | 4 | 5
C4 LD R10, (16)10(R8) | 2 | 3 | 4 | 5 | 6
C8 DOR R11, R9, R10 | 3 | 4 | 5 | 6 | 7
CC SD R11, O(R8) | 4 | 5 | 6 | 7 | 
At cycle 3, both IF and EX need ALU
  IF : PC  PC +4
  EX: ALUOut1  A + Imm
which stage gets the ALU first?

## Slide 61: Processor Pipelining – Structural Hazards
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 | 4 | 5
C4 LD R10, (16)10(R8) | 2 | 3 | 4 | 5 | 6
C8 DOR R11, R9, R10 | 3 | 4 | 5 | 6 | 7
CC SD R11, O(R8) | 4 | 5 | 6 | 7 | 
At cycle 4, both IF and MEM need memory port
  IF : IR M[PC]
  MEM: M[ALUOut1]  B
Which stage get memory port first?

## Slide 62: Processor Pipelining – Structural Hazards
Mitigation: Add multiple resources
  One ALU for IF stage, another ALU for EX stage
  One memory port for IF, another port for MEM stage
Generally, CPUs have several replications of resources and structural hazards rarely occur for common applications

## Slide 63: Processor Pipelining – Data Hazards
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 | 4 | 5
C4 LD R10, (16)10(R8) | 2 | 3 | 4 | 5 | 6
C8 DOR R11, R9, R10 | 3 | 4 | 5 | 6 | 7
CC SD R11, O(R8) | 4 | 5 | 6 | 7 | 
Read After Write (RAW) hazard
  Instruction at C8 depends on R9 and R10
  The value of R10 is not updated until cycle 6
  Instruction at C8 reads it in ID stage at cycle 5
  Instruction at C8 gets wrong data

## Slide 64: Processor Pipelining – Data Hazards
Instruction | IF | ID | EX | MEM | WB
C0 LD R9, 8(R8) | 1 | 2 | 3 | 4 | 5
C4 LD R10, (16)10(R8) | 2 | 3 | 4 | 5 | 6
C8 DOR R11, R9, R10 | 3 | 4 | 5 | 6 | 7
CC SD R11, O(R8) | 4 | 5 | 6 | 7 | 
Data Forwarding
  Send data from MEM to EX stage when it is needed
    In MEM, value of R10 is in LMD register
  EX gets value of R10 in cycle 5 and dismisses value read in cycle 4 during ID stage

## Slide 65: Processor Pipelining – Data Hazards
Instruction Reordering
  During compilation, find independent instructions
  Put them in between instructions that would lead to RAW hazards

## Slide 66: Processor Pipelining – Data Hazards
Instruction Reordering
Instruction
C0 LD R9, 8(R8)
C4 LD R10, (16)10(R8)
C8 DOR R11, R9, R10
CC SD R11, O(R8)
D0 LD R13, 0(R14)
D4 DADD R17, R0, R0
Instructions at C4 and C8 lead to RAW
Instruction at D0 is independent of instructions C4, C8, CC

## Slide 67: Processor Pipelining – Data Hazards
Instruction Reordering
Instruction
C0 LD R9, 8(R8)
C4 LD R10, (16)10(R8)
C8 LD R13, 0(R14)
CC DADD R17, R0, R0
D0 DOR R11, R9, R10
D4 SD R11, O(R8)
Instructions at C4 and C8 lead to RAW
Instruction at D0 is independent of instructions C4, C8, CC
Put (previously D0) independent instruction in between RAW hazard instructions to give one more cycle between them
IF | ID | EX | MEM | WB
1 | 2 | 3 | 4 | 5
2 | 3 | 4 | 5 | 6
3 | 4 | 5 | 6 | 7
4 | 5 | 6 | 7 | 8
5 | 6 | 7 | 8 | 9
6 | 7 | 8 | 9 | 

## Slide 68: Processor Pipelining – Branch Hazards
Branch instruction BEQZ at E0 checks the condition and gets the target at EX stage in cycle 6
To keep pipeline full, next instruction needs to be fetched at cycle 5
But
  We don’t know if the branch is taken or the target address until cycle 6
  How do know what instruction to fetch for IF at cycle 5?
Instruction | IF | ID | EX | MEM | WB
E0 BEQZ R8, (-3)10 | 4 | 5 | 6 |  | 
E4 DOR R11, R9, R10 | 5 | 6 | 7 | 8 | 9
Is this correct?

## Slide 69: Processor Pipelining – Branch Hazards
Mitigation 1: Pipeline bubble
  Stall pipeline until branch instruction finishes EX stage
  Does not maximize pipeline throughput
Mitigation 2: Branch delay slot
  Similar to instruction re-ordering
  Put instruction that is executes whether branch is taken or not right after branch
Mitigation 2: Branch prediction
  Predict if branch is taken/not taken
  Fetch next instruction based on prediction
  When branch completes, check if prediction was correct
  Update his tory for better accuracy for next time
Prediction over 99% accurate

## Slide 70: Topics Covered
3 instruction formats in MIPS
  R, I, and J-formats
Instruction formatting fundamental in CPU design
5 main steps to execute instruction
  Fetch
  Decode
  Execute
  Memory
  WriteBack
CPU Pipelining